Microprocessor

8085

Ex . No :                                                     8 – Bit Addition Without Carry	                                    Page No :

Aim :

To write an assembly language program to perform 8 – bit addition without carry using 8085 microprocessor.

Apparatus Required :

8085 trainer kit, keyboard

Algorithm :

- Load the content of memory address 4150 to accumulator.

- Move the content of accumulator to B register.

- Load the content of memory address 4151 to accumulator.

- Add the content of B register with accumulator.

- The result is stored in 4152.

- Halt the program.

Program :

| ADDRESS | MNEMONICS | OPCODE | COMMENTS |
| --- | --- | --- | --- |
| 4100 | LDA 4150 | 3A | Get the content of 4150 for Acc. |
| 4101 |  | 50 |  |
| 4102 |  | 41 |  |
| 4103 | MOV B,A | 47 | Move the content of Acc to B register. |
| 4104 | LDA 4151 | 3A | Get the content of 4151 for Acc. |
| 4105 |  | 51 |  |
| 4106 |  | 41 |  |
| 4107 | ADD B | 80 | Add B Register with Acc. |
| 4108 | STA 4152 | 32 | Store the content of Acc to the location 4152 |
| 4109 |  | 52 |  |
| 410A |  | 41 |  |
| 410B | HLT | 76 | Halt the program. |

Result :

Thus the program for 8 – bit addition without carry was executed and verified successfully using 8085 microprocessor.

Ex . No :                                                     8 – Bit Subtraction Without Carry	                                    Page No :

Aim :

To write an assembly language program to perform 8 – bit subtraction without carry using 8085 microprocessor.

Apparatus Required :

8085 trainer kit, keyboard

Algorithm :

- The data is moved immediately into Acc.

- The data is moved immediately into B Register.

- Subtract the content of B register with accumulator.

- The result is stored in 4152.

- Halt the program.

Program :

| ADDRESS | MNEMONICS | OPCODE | COMMENTS |
| --- | --- | --- | --- |
| 4100 | MVI A, 05 | 3E | First operand stored in accumulator. |
| 4101 |  | 05 |  |
| 4102 | MVI B,02 | 06 | Second operand stored in B Register. |
| 4103 |  | 02 |  |
| 4104 | SUB B | 90 | Subtract the content of B reg. with the content of Acc. |
| 4105 | STA 4150 | 32 | Store the content of Acc to the location 4150. |
| 4106 |  | 50 |  |
| 4107 |  | 41 |  |
| 4108 | HLT | 76 | Halt the program. |

Result :

Thus the program for 8 – bit subtraction without carry was executed and verified successfully using 8085 microprocessor.

Ex . No :                                                          8 – Bit Addition With Carry	                                    Page No :

Aim :

To write an assembly language program to perform 8 – bit addition with carry using 8085 microprocessor.

Apparatus Required :

8085 trainer kit, keyboard

Algorithm :

- Initialize any one register for carry with data 00H.

- Move the first operand to the accumulator.

- Add the another operand with the accumulator.

- If carry flag is set, then increment the carry by one.

- Store the accumulator content and carry content in memory location.

- Halt the program.

Program :

| ADDRESS | MNEMONICS | OPCODE | COMMENTS |
| --- | --- | --- | --- |
| 4100 | MVI C,00 | 0E | Initialize carry register as 00H. |
| 4101 |  | 00 |  |
| 4102 | MVI A,A1 | 3E | First operand stored in Acc. |
| 4103 |  | A1 |  |
| 4104 | MVI B,72 | 06 | Second operand stored in B register. |
| 4105 |  | 72 |  |
| 4106 | ADD B | 80 | Add the content of B register with the content of Acc. |
| 4107 | JNC 410B | D2 | If carry doesn’t exist jump on the location 410B. |
| 4108 |  | 0B |  |
| 4109 |  | 41 |  |
| 410A | INR C | 0C | Increment content of C Register. |
| 410B | STA 4150 | 32 | Store the content of Acc to the location 4150 |
| 410C |  | 50 |  |
| 410D |  | 41 |  |
| 410E | MOV A,C | 79 | Move the content of C register to accumulator |
| 410F | STA 4151 | 32 | Store the content of Acc to the location 4151. |
| 4110 |  | 51 |  |
| 4111 |  | 41 |  |
| 4112 | HLT | 76 | Halt the program. |

Result :

Thus the program for 8 – bit addition with carry was executed and verified successfully using 8085 microprocessor.

Ex . No :                                                          8 – Bit Subtraction With Carry	                                    Page No :

Aim :

To write an assembly language program to perform 8 – bit subtraction with carry using 8085 microprocessor.

Apparatus Required :

8085 trainer kit, keyboard

Algorithm :

- Initialize any one register for carry with data 00H.

- Move the first operand to the accumulator.

- Subtract the another operand with the accumulator.

- If carry flag is set, then increment the carry by one.

- Store the accumulator content and carry content in memory location.

- Halt the program.

Program :

| ADDRESS | MNEMONICS | OPCODE | COMMENTS |
| --- | --- | --- | --- |
| 4100 | MVI C,00 | 0E | Initialize carry register as 00H. |
| 4101 |  | 00 |  |
| 4102 | MVI A,05 | 3E | First operand stored in Acc. |
| 4103 |  | A1 |  |
| 4104 | MVI B,09 | 06 | Second operand stored in B register. |
| 4105 |  | 72 |  |
| 4106 | SUB B | 90 | Subtract the content of B register with the content of Acc. |
| 4107 | JNC 410B | D2 | If carry doesn’t exist jump on the location 410B. |
| 4108 |  | 0B |  |
| 4109 |  | 41 |  |
| 410A | INR C | 0C | Increment content of C Register. |
| 410B | STA 4150 | 32 | Store the content of Acc to the location 4150 |
| 410C |  | 50 |  |
| 410D |  | 41 |  |
| 410E | MOV A,C | 79 | Move the content of C register to accumulator |
| 410F | STA 4151 | 32 | Store the content of Acc to the location 4151. |
| 4110 |  | 51 |  |
| 4111 |  | 41 |  |
| 4112 | HLT | 76 | Halt the program. |

Result :

Thus the program for 8 – bit subtraction with carry was executed and verified successfully using 8085 microprocessor.

Ex . No :                                                              8 – Bit Multiplication	                                                Page No :

Aim :

To write an assembly language program to perform the multiplication of two

8- bit data using 8085 microprocessor.

Apparatus Required :

8085 trainer kit, keyboard

Algorithm :

- Initialize the content of Acc to 00H.

- Move the first operand to B register and Second operand to C register.

- Add the content of B register with accumulator.

- Decrement the C register.

- If zero doesn’t exit then jump to B register.

- Store the result in accumulator.

- Halt the program.

Program :

| ADDRESS | MNEMONICS | OPCODE | COMMENTS |
| --- | --- | --- | --- |
| 4100 | MVI A,00 | 3E | Initialize the accumulator as 00H. |
| 4101 |  | 00 |  |
| 4102 | MVI B,11 | 06 | Move the first operand to B register. |
| 4103 |  | 11 |  |
| 4104 | MVI C,11 | 0E | Move the second operand to C register. |
| 4105 |  | 11 |  |
| 4106 | MVI D,00 | 16 | Initialize the D register as 00H. |
| 4107 |  | 00 |  |
| 4108 | L2:ADD B | 80 | Add the content of B register to accumulator. |
| 4109 | JNC 410D:L1 | D2 | If the carry doesn’t exist jump to 410D. |
| 410A |  | 0D |  |
| 410B |  | 41 |  |
| 410C | INR D | 14 | Increment the D Register by one. |
| 410D | L1:DCR C | 0D | Decrement the C Register by one. |
| 410E | JNZ 4108:L2 | C2 | If no zero exit then jump to 4108. |
| 410F |  | 08 |  |
| 4110 |  | 41 |  |
| 4111 | STA 4150 | 32 | Store the content of Acc to the location 4150. |
| 4112 |  | 50 |  |
| 4113 |  | 41 |  |
| 4114 | MOV A,D | 7A | Move the content of D register to the accumulator. |
| 4115 | STA 4151 | 32 | Store the content of Acc to the location 4151. |
| 4116 |  | 51 |  |
| 4117 |  | 41 |  |
| 4118 | HLT | 76 | Halt the program. |

Result :

Thus the program for 8 – bit multiplication was executed and verified successfully using 8085 microprocessor.

Ex . No :                                                                 8 – Bit Division	                                                Page No :

Aim :

To write an assembly language program to perform the division of two

8- bit data using 8085 microprocessor.

Apparatus Required :

8085 trainer kit, keyboard

Algorithm :

- Load the content of memory address 4150 to Accumulator and move it to B reg.

- Load the content of memory address 4151 to Accumulator.

- Initialize any one register for carry with data 00H.

- Compare B register with Accumulator.

- Jump on to the carry, if exists then store the result on the location.

- Subtract the content of B register from Accumulator.

- Increment the content of C register.

- Compare B register with Acc. If carry doesn’t exist jump to 4109.

- Store the result in 4153(remainder).

- Move the content of C register to Acc. Store the result in 4152(quotient).

- Halt the program

Program :

| ADDRESS | MNEMONICS | OPCODE | COMMENTS |
| --- | --- | --- | --- |
| 4100 | LDA 4150 | 3A | Load the content of 4150 to Acc(divisor). |
| 4101 |  | 50 |  |
| 4102 |  | 41 |  |
| 4103 | MOV B,A | 47 | Move the content of Acc to B register. |
| 4104 | LDA 4151 | 3A | Load the content of 4151 to Acc(divident). |
| 4105 |  | 51 |  |
| 4106 |  | 41 |  |
| 4107 | MVI C,00 | 0E | Initialize carry register C as 00H. |
| 4108 |  | 00 |  |
| 4109 | CMP B | B8 | Compare B register with Acc. |
| 410A | JC 4113 | DA | Jump carry on 4113. |
| 410B |  | 13 |  |
| 410C |  | 41 |  |
| 410D | SUB B | 90 | Subtract the content of B register with Acc. |
| 410E | INR C | 0C | Increment the content of C register. |
| 410F | CMP B | B8 | Compare B register with Acc. |
| 4110 | JNC 4109 | D2 | If carry doesn’t exist jump to 4109. |
| 4111 |  | 09 |  |
| 4112 |  | 41 |  |
| 4113 | STA 4153 | 32 | Store the result in 4153(remainder). |
| 4114 |  | 53 |  |
| 4115 |  | 41 |  |
| 4116 | MOV A,C | 79 | Move the content of C register to Acc. |
| 4117 | STA 4152 | 32 | Store the result in 4152(quotient). |
| 4118 |  | 52 |  |
| 4119 |  | 41 |  |
| 411A | HLT | 76 | Halt the program |

Result :

Thus the program for 8 – bit division was executed and verified successfully using 8085 microprocessor.

Ex . No :                                     Interfacing Of 8279 With 8085 Microprocessor Kit    	                       Page No :

Aim :

To write an assembly language program to illustrate IC 8279 microprocessor kit also to display rolling message “HELP US”.

Apparatus Required :

8085 trainer kit, keyboard, 8279 Interfacing board.

Algorithm :

- Initialize 8279 a) display key board mode is set   b) clear mode

- Before sending codes to display ram (or) write ram control word should be sent.

- Write the data to be displayed to the data register.

Program :

| ADDRESS | LABEL | MNEMONICS | OPCODE | COMMENTS |
| --- | --- | --- | --- | --- |
| 4100 | START | LXI H,412CH | 21 | Set Pointer To 412CH |
| 4101 |  |  | 2C |  |
| 4102 |  |  | 41 |  |
| 4103 |  | MVI D,0F H | 16 | Initialize the count |
| 4104 |  |  | 0F |  |
| 4105 |  | MVI A,10 | 3E | Move The Count To Acc |
| 4106 |  |  | 10 |  |
| 4107 |  | OUT C2 | D3 | Set mode and display |
| 4108 |  |  | C2 |  |
| 4109 |  | MVI A,CCH | 3E | Clear display |
| 410A |  |  | CC |  |
| 410B |  | OUT C2 | D3 |  |
| 410C |  |  | C2 |  |
| 410D |  | MVI A,90H | 3E | Write display |
| 410E |  |  | 90 |  |
| 410F |  | OUT C2 | D3 | Output display |
| 4110 |  |  | C2 |  |
| 4111 | L | MOV A,M | 7E | Move memory count to Acc |
| 4112 |  | OUT C0 | D3 |  |
| 4113 |  |  | C0 |  |
| 4114 |  | CALL DELAY 411F | CD |  |
| 4115 |  |  | 1F |  |
| 4116 |  |  | 41 |  |
| 4117 |  | INX H | 23 | Increment the pointer |
| 4118 |  | DCR D | 15 | Decrement the pointer |
| 4119 |  | JNZ 4111(L) | C2 | Jump if no zero to 4111 |
| 411A |  |  | 11 |  |
| 411B |  |  | 41 |  |
| 411C |  | JMP 4100 | C3 | Display the next chr. |
| 411D |  |  | 00 |  |
| 411E |  |  | 41 |  |
| 411F | DELAY | MVI B,A0H | 06 | Move the count of B register |
| 4120 |  |  | A0 |  |
| 4121 | L1 | MVI C,FFH | 0E | Move the count of C register |
| 4122 |  |  | FF |  |
| 4123 | L2 | DCR C | 0D | Decrement the C register |
| 4124 |  | JNZ 4123 (L2) | C2 | Jump no zero to 4123 |
| 4125 |  |  | 23 |  |
| 4126 |  |  | 41 |  |
| 4127 |  | DCR B | 05 | Decrement the B register |
| 4128 |  | JNZ 4121(L1) | C2 | Jump no zero to 4121 |
| 4129 |  |  | 21 |  |
| 412A |  |  | 41 |  |
| 412B |  | RET | C9 | Reset the program. |
| 412C |  |  | FF |  |
| 412D |  |  | FF |  |
| 412E |  |  | FF |  |
| 412F |  |  | FF |  |
| 4130 |  |  | FF |  |
| 4131 |  |  | FF |  |
| 4132 |  |  | FF |  |
| 4133 |  |  | FF |  |
| 4134 |  |  | 98 |  |
| 4135 |  |  | 68 |  |
| 4136 |  |  | 7C |  |
| 4137 |  |  | C8 |  |
| 4138 |  |  | 1C |  |
| 4139 |  |  | 29 |  |
| 413A |  |  | FF |  |
| 413B |  |  | FF |  |

Result :

Thus the assembly language program  to illustrate IC 8279 with 8085 microprocessor kit to display rolling massage ‘HELPUS’ was executed and verified.

Ex . No :                                  Interfacing Of Programmable Interrupt Controller (8259)    	          Page No :

Aim :

To write an ALP program for 8259, to enable the IR0 switch using 8085 microprocessor.

Apparatus Required :

1.8085 trainer kit

2. Keyboard

3.8259 interface board

4.50 core cable

Algorithm :

- Initialize the 8259 IC.

- Set the interrupt memory location.

- Write any one simple program in interrupt memory location.

- Enable the corresponding interrupt switch.

- After the enabling of IR0 switch program counter fetch ISR starting address, execute the ISR program.

- Check the result and halt the program.

Program :

| ADDRESS | MNEMONICS | OPCODE | COMMENTS |
| --- | --- | --- | --- |
| 4100 | MVI A,17 | 3E | Move the data to accumulator |
| 4101 |  | 17 |  |
| 4102 | OUT C0H | D3 | Out the data |
| 4103 |  | C0 |  |
| 4104 | MVI A,50H | 3E | Move the data to accumulator |
| 4105 |  | 50 |  |
| 4106 | OUT C2H | D3 | Out the data |
| 4107 |  | C2 |  |
| 4108 | MVI A,00H | 3E | Move the data to accumulator |
| 4109 |  | 00 |  |
| 410A | OUT C2H | D3 |  |
| 410B |  | C2 |  |
| 410C | MVI A,FEH | 3E | Move the data to accumulator |
| 410D |  | FE |  |
| 410E | OUT C2H | D3 | Out the data |
| 410F |  | C2 |  |
| 4110 | HLT | 76 | Halt the program |

Subroutine Program :

| ADDRESS | MNEMONICS | OPCODE | COMMENTS |
| --- | --- | --- | --- |
| 5000 | MVI A,05 | 3E | First operand stored in accumulator |
| 5001 |  | 05 |  |
| 5002 | MVI B,02 | 06 | Second operand stored in B register |
| 5003 |  | 02 |  |
| 5004 | SUB B | 90 | subtract content of B register with the content of accumulator |
| 5005 | STA 4150 | 32 | Store the content of accumulator to the location of 4150 |
| 5006 |  | 50 |  |
| 5007 |  | 41 |  |
| 5008 | HLT | 76 | Halt the Program |

Result :

Thus the assembly language program for interfacing of programmable interrupt controller (8259) was executed and verified using 8085 microprocessor.

Ex. No :                                           Interfacing  of  8255 with 8085 Microprocessor                              Page No :

Aim :

To write an assembly language program to initialize port A as an input port in mode-0 and to input the data set by the SPDT switches through port A and store the data.

Apparatus Required :

8085 trainer kit, keyboard, 8255 Interfacing board.

Algorithm :

- Initialize 8255 (Port A as Input).

- Out the data to 8255 control register address.

- Read the port A data (switch).

- Store the data to memory 4500H.

- Halt the program.

Program :

| ADDRESS | MNEMONICS | OPCODE | COMMENTS |
| --- | --- | --- | --- |
| 4100 | MVI A, 90 | 3E | Initialize the accumulator as 90H |
| 4101 |  | 90 |  |
| 4102 | OUT 0C6H | D3 | Out to control port |
| 4103 |  | C6 |  |
| 4104 | IN 0C0H | DB | Read port A |
| 4105 |  | CO |  |
| 4106 | STA 4500 H | 32 | Store it in 4500H |
| 4107 |  | 00 |  |
| 4108 |  | 45 |  |
| 4109 | HLT | 76 | Halt the program. |

Result :

Thus the program for interfacing 8255 by keeping port A as an input port in mode-0 was executed and verified using 8085 microprocessor.

Ex . No :                                            Interfacing of  8255 with 8085 Microprocessor	                       Page No:

:

Aim :

To write an assembly language program to initialize port A as Input port and port B as Output port in mode-0, to input the data at port A as set by the SPDT switches and to output the same data to port B to glow the LED accordingly.

Apparatus Required :

8085 trainer kit, keyboard, 8255 Interfacing Board.

Algorithm :

- Initialize 8255 (Port A - Input, Port B - Output).

- Out the data to 8255 control register address.

- Read the port A data (switch).

- Write the data to Port B(LED).

- Halt the program.

Program :

| ADDRESS | MNEMONICS | OPCODE | COMMENTS |
| --- | --- | --- | --- |
| 4100 | MVI A, 90 | 3E | Initialize port A as an input. |
| 4101 |  | 90 |  |
| 4102 | OUT 0C6H | D3 | Out to control port |
| 4103 |  | C6 |  |
| 4104 | IN 0C0H | DB | Read port A into control port. |
| 4105 |  | CO |  |
| 4106 | OUT 0C2H | D3 | Store it in 4500H |
| 4107 |  | C2 |  |
| 4108 | HLT | 76 | Halt the program. |

Result :

Thus the program for interfacing 8255 by keeping port A as an input port and port B as output port and glowing LED’s was executed and verified using 8085 microprocessor.

Microprocessor

8086

Ex . No :                                          Generation of Square Wave using Timer(8253)   	                      Page No :

Aim :

To write an ALP program to generate square wave using 8253 timer IC with 8086.

Apparatus Required :

1.8086 microprocessor kit

2. Keyboard.

3. 8253 Interface Board.

4.50 core cable

5. Power chord

Algorithm :

- Initialize accumulator lower order with data 36.

- Out the data to 8253 control register.

- Move the data 0A to accumulator Lower order.

- Out the data to 8253 Data register.

- Move the data 00 to accumulator Lower order.

- Out the data to 8253 Data register.

- Halt the Program.

Program :

| ADDRESS | MNEMONICS | OPCODE | COMMENTS |
| --- | --- | --- | --- |
| 1000 | MOV AL,36 | B0 |  |
| 1001 |  | 36 |  |
| 1002 | OUT CE,AL | E6 |  |
| 1003 |  | CE |  |
| 1004 | MOV AL,0A | B0 |  |
| 1005 |  | 0A |  |
| 1006 | OUT C8,AL | E6 |  |
| 1007 |  | C8 |  |
| 1008 | MOV AL,00 | B0 |  |
| 1009 |  | 00 |  |
| 100A | OUT C8,AL | E6 |  |
| 100B |  | C8 |  |
| 100C | HLT | F4 |  |

Result :

Thus the assembly language program for generation of square wave using timer was executed and verified successfully using 8086 microprocessor.

Ex . No :                                      Interfacing of  Traffic Light Control with 8086.                                  Page No:

Aim :

To write an ALP program to generate square wave using 8253 timer IC with 8086.

Apparatus Required :

1.8086 microprocessor kit

2. Keyboard.

3. 8253 Interface Board.

Algorithm :

- Initialize 8255 with corresponding data (Port A, B, C- output).

- Out the data to Control Register Address.

- Store corresponding Direction data’s in the memory location 1073.

- Out the data in the Required ports continuously with delay .

5.    Halt the Program.

Program :

| ADDRESS | LABEL | MNEMONICS | OPCODE | COMMENTS |
| --- | --- | --- | --- | --- |
| 1000 | START | MOV AL,80H | C6 | Move the data to AL. |
| 1001 |  |  | C0 |  |
| 1002 |  |  | 80 |  |
| 1003 |  | OUT CNTRL,AL | E6 | Out the data to CNTRL. |
| 1004 |  |  | 26 |  |
| 1005 | REPEAT | MOV BX, LOOKUP | C7 | Move the data from LOOKUP to BX register. |
| 1006 |  |  | C3 |  |
| 1007 |  |  | 73 |  |
| 1008 |  |  | 10 |  |
| 1009 |  | MOV S1,LABEL | C7 | Move the data from LABEL to S1 register. |
| 100A |  |  | C6 |  |
| 100B |  |  | 7F |  |
| 100C |  |  | 10 |  |
| 100D |  | CALL OUT | E8 | Call the OUT. |
| 100E |  |  | 33 |  |
| 100F |  |  | 00 |  |
| 1010 |  | MOV AL,[S1] | 8A | Move the data from S1 to AL register. |
| 1011 |  |  | 04 |  |
| 1012 |  | OUT PORT A,AL | E6 | Out the data from AL to port A. |
| 1013 |  |  | 20 |  |
| 1014 |  | CALL DELAY1 | E8 | Call the DELAY1. |
| 1015 |  |  | 4D |  |
| 1016 |  |  | 00 |  |
| 1017 |  | INC S1 | 46 | Increment S1 value. |
| 1018 |  | INC BX | 43 | Increment BX register value. |
| 1019 |  | CALL OUT | E8 | Call the OUT. |
| 101A |  |  | 27 |  |
| 101B |  |  | 00 |  |
| 101C |  | MOV AL,[S1] | 8A | Move the data fr0m S1 to AL register. |
| 101D |  |  | 04 |  |
| 101E |  | OUT PORT B,AL | E6 | Out the AL data to port B |
| 101F |  |  | 22 |  |
| 1020 |  | CALL DELAY1 | E8 | Call the DELAY1. |
| 1021 |  |  | 41 |  |
| 1022 |  |  | 00 |  |
| 1023 |  | INC S1 | 46 | Increment the S1 value. |
| 1024 |  | INC BX | 43 | Increment the BX register value. |
| 1025 |  | CALL OUT | E8 | Call the OUT. |
| 1026 |  |  | 1B |  |
| 1027 |  |  | 00 |  |
| 1028 |  | MOV AL,[S1] | 8A | Move the data from S1 the AL register. |
| 1029 |  |  | 04 |  |
| 102A |  | OUT PORT C,AL | E6 | Out the AL data to port C. |
| 102B |  |  | 24 |  |
| 102C |  | CALL DELAY1 | E8 | Call the DELAY1. |
| 102D |  |  | 35 |  |
| 102E |  |  | 00 |  |
| 102F |  | INC S1 | 46 | Increment the S1 value. |
| 1030 |  | INC BX | 43 | Increment the BX register value. |
| 1031 |  | CALL OUT | E8 | Call the OUT. |
| 1032 |  |  | 0F |  |
| 1033 |  |  | 00 |  |
| 1034 |  | MOV AL,[S1] | 8A | Move the data from S1 the AL register. |
| 1035 |  |  | 04 |  |
| 1036 |  | OUT PORT C,AL | E6 | Out the AL data to port C. |
| 1037 |  |  | 24 |  |
| 1038 |  | INC S1 | 46 | Increment the S1 value. |
| 1039 |  | MOV AL,[S1] | 8A |  |
| 103A |  |  | 04 |  |
| 103B |  | OUT PORT C,AL | E6 | Move the data from S1 the AL register. |
| 103C |  |  | 20 |  |
| 103D |  | CALL DELAY1 | E8 | Call the DELAY1. |
| 103E |  |  | 24 |  |
| 103F |  |  | 00 |  |
| 1040 |  | JMP REPEAT | E9 | Jump to REPEAT. |
| 1041 |  |  | C2 |  |
| 1042 |  |  | FF |  |
| 1043 | OUT | MOV AL,[BX] | 8A | Move the data from BX register to AL register. |
| 1044 |  |  | 07 |  |
| 1045 |  | OUT PORT C,AL | E6 | Out the AL data to port C. |
| 1046 |  |  | 24 |  |
| 1047 |  | INC BX | 43 | Increment the BX register value. |
| 1048 |  | MOV AL,[BX] | 8A | Move the data from BX register to AL register. |
| 1049 |  |  | 07 |  |
| 104A |  | OUT PORT B,AL | E6 | Out the AL data to port B. |
| 104B |  |  | 22 |  |
| 104C |  | INC BX | 43 | Increment the BX register value. |
| 104D |  | MOV AL,[BX] | 8A | Move the data from BX register to AL register. |
| 104E |  |  | 07 |  |
| 104F |  | OUT PORT A,AL | E6 | Out the AL data to port A. |
| 1050 |  |  | 20 |  |
| 1051 |  | CALL DELAY | E8 | Call the DELAY. |
| 1052 |  |  | 01 |  |
| 1053 |  |  | 00 |  |
| 1054 |  | RET | C3 | Return to START. |
| 1055 | DELAY | MOV D1,00040H | C7 | Move the data to D1 register. |
| 1056 |  |  | C7 |  |
| 1057 |  |  | 40 |  |
| 1058 |  |  | 00 |  |
| 1059 | A | MOV DX, 0FFFFH | C7 | Move the data to DX register. |
| 105A |  |  | C2 |  |
| 105B |  |  | FF |  |
| 105C |  |  | FF |  |
| 105D | A1 | DEC DX | 4A | Decrement DX register value. |
| 105E |  | JNZ A1 | 75 | If not zero, then jump to A1. |
| 105F |  |  | FD |  |
| 1060 |  | DEC D1 | 4F | Decrement the D1 value. |
| 1061 |  | JNZ A | 75 | Decrement DX register value. |
| 1062 |  |  | F6 |  |
| 1063 |  | RET | C3 | Return. |
| 1064 | DELAY1 | MOV D1, 00051H | C7 | Move the data to D1 register. |
| 1065 |  |  | C7 |  |
| 1066 |  |  | 15 |  |
| 1067 |  |  | 00 |  |
| 1068 | B | MOV DX, 0FFFFH | C7 | Move the data to DX register. |
| 1069 |  |  | C2 |  |
| 106A |  |  | FF |  |
| 106B |  |  | FF |  |
| 106C | B1 | DEC DX | 4A | Decrement DX register value. |
| 106D |  | JNZ B1 | 75 | If not zero, then jump to B1. |
| 106E |  |  | FD |  |
| 106F |  | DEC D1 | 4F | Decrement D1 register value. |
| 1070 |  | JNZ B | 75 | If not zero, then jump to B. |
| 1071 |  |  | F6 |  |
| 1072 |  | RET | C3 | Return. |
| 1073 | LOOKUP | DB 12 27 44 10 2B 92 10 9D 84 48 2E 84 | 12 |  |
| 1074 |  |  | 27 |  |
| 1075 |  |  | 44 |  |
| 1076 |  |  | 10 |  |
| 1077 |  |  | 2B |  |
| 1078 |  |  | 92 |  |
| 1079 |  |  | 10 |  |
| 107A |  |  | 9D |  |
| 107B |  |  | 84 |  |
| 107C |  |  | 48 |  |
| 107D |  |  | 2E |  |
| 107E |  |  | 84 |  |
| 107F | LABEL | DB 48 4B 20 49 O4 | 48 |  |
| 1080 |  |  | 4B |  |
| 1081 |  |  | 20 |  |
| 1082 |  |  | 49 |  |
| 1083 |  |  | 04 |  |
| 1084 |  | END |  |  |

Result :

Thus the assembly language program to enable the Traffic Light Controller using 8086 microprocessor was verified and executed successfully.

Ex . No :                                                            Create a file using MASM  Software	                          Page No :

Aim :

To create a file using MASM software in the required directory.

Apparatus Required :

1. Personal computer

2. MASM software

Algorithm :

- Initialize Code (ROM) and Data (RAM) Segment.

- Store the file name in the address 1300h.

- Call File attributes for Read only.

- Call the DOS Function address for File creation.

- Call the DOS Function address for File termination.

- Call the DOS address for interrupt the Processor.

- Halt the Program.

Program :

Code segment

assume cs:code,ds:data

org 1000h

mov ax, data

mov ds,ax                                  ; Data segment Initialization.

mov dx, 1300h                          ; Data’s for file name.

mov cx,0000h                           ; File attributes.

mov ah,3ch                               ; System call for file creation

int 21h

mov ah,4ch                               ; System call for program termination.

int 21h

int 20h

code ends

data segment

org 1300h

db ‘test.asm’

data ends

end.

File Attributes

Cx = 0000h              ; Read only file.

; Hidden file.

; System file.

Result :

Thus to create a file using MASM software in the required directory was executed successfully.

Ex . No :                                                            Delete a file using MASM  	                                  Page No :

Aim :

To delete a file using MASM software in the required directory

Apparatus Required :

1. Personal computer

2. MASM software

Algorithm :

1.  Initialize Code (ROM) and Data (RAM) Segment.

2.  Store the Required file name in the address 1300h.

3.  Call the DOS Function address for File Delete.

- Call the DOS Function address for File termination.

- Call the DOS address for interrupt the Processor.

- Halt the Program.

Program :

Code segment

assume cs:code,ds:data

org 1000h

mov ax, data

mov ds,ax                                  ; Data segment Initialization.

mov dx, 1300h

mov ah,41h                               ; Dos call for file delete.

int 21h

mov ah,4ch                               ; Dos call for program termination.

int 21h

code ends

data segment

org 1300h

db ‘test.asm’

data ends

end.

Result :

Thus to delete a file using MASM software in the required directory was executed successfully.

Ex . No :                                An ALP to read a key code from keyboard using MASM  	          Page No :

Aim :

To Display the ASCII code for Key, while pressing the Keyboard

Apparatus Required :

1. Personal computer

2. MASM software

Algorithm :

1.  Initialize Code (ROM) and Data (RAM) Segment.

2. Move the address 1200 to soure index register, for storing the ASCII data.

3. Call the DOS Function address for Key Read.

4.  Store the ASCII data in Address 1200h.

5. Call the DOS Function address for Program termination.

6. Halt the Program.

Program :

Code segment

assume cs:code,ds:code

org 1000h

mov si, 1200h

mov ah,00h                               ; BIOS call for key status word.

int 16h

mov [si],al                                ; Store the key code.

inc si

mov ah,4ch                               ; Dos call for program termination.

int 21h

code ends

end.

Result :

Thus to Display the ASCII code for Key, while pressing the Keyboard was executed successfully.

Ex . No :                                              An ALP to clear the screen using MASM  	                      Page No :

Aim :

To clear the Output Screen (DOS window) using the MASM software.

Apparatus Required :

1. Personal computer

2. MASM software

Algorithm :

1.  Initialize Code (ROM) and Data (RAM) Segment.

2. Move the Data to CX register to select the Row and Column.

3. Call the DOS Function address for selecting corners.

4. Call the DOS Function address for Scroll page down.

5. Call the DOS Function address to select the cursor position.

6 Call the DOS Function address for Program termination.

7. Halt the Program.

Program :

Code segment

assume cs:code,ds:code

org 1000h

mov cx, 0000h                  ; Row, column of upper left corner of window to scroll.

mov dx,184fh                   ; Row, column of lower right corner of window.

mov ah, 07h                      ; System call for scroll page down.

mov bh, 07h

int 10h

mov ah,02h                       ; System call for set cursor position.

mov bh,00h

mov dx,0000h

int 10h

mov ah,4ch

int 21h

code ends

end.

Result :

Thus to clear the Output Screen (DOS window) using the MASM software was executed successfully.

Microcontroller

8051

Ex . No :                                                           Interfacing of  Stepper Motor    	                                  Page No :

Aim :

To write an ALP program for interfacing stepper motor control using 8051 microcontroller.

Apparatus Required :

1.8051 microcontroller kit

2. Keyboard

3.50 core cable

4. Stepper motor Interface board

5. Stepper motor

6. Power chord

Algorithm :

- Initialize the address 4500H with forward or reverse direction data’s.

- Load the counter value.

- Move the data to stepper motor connected address.

- Call Delay.

- Decrement the counter value as well as send the next data to port address upto counter reaches zero.

- Goto step1.

- Halt the program.

Program :

| ADDRESS | LABEL | MNEMONICS | OPCODE | COMMENTS |
| --- | --- | --- | --- | --- |
| 4100 | START | MOV DPTR, #4500H | 90 | Move the content of 4500H to DPTR |
| 4101 |  |  | 45 |  |
| 4102 |  |  | 00 |  |
| 4103 |  | MOV R0, #04 H | 78 | Move the 04 content to R0 register. |
| 4104 |  |  | 04 |  |
| 4105 | J0 | MOV X A,@DPTR | E0 | Move the content of DPTR to Acc(16 bit). |
| 4106 |  | PUSH DPH | C0 | Push the DP from stack ptr. |
| 4107 |  |  | 83 |  |
| 4108 |  | PUSH DPL | C0 | Push the DP from L Register. |
| 4109 |  |  | 82 |  |
| 410A |  | MOV DPTR, #FFC0H | 40 | Move FF content to DPTR. |
| 410B |  |  | FF |  |
| 410C |  |  | C0 |  |
| 410D |  | MOV R2, #04 H | 7A | Move 04 content to R2 reg. |
| 410E |  |  | 04 |  |
| 410F |  | MOV R1, # 0FH | 79 | Move 0F content to R1 reg. |
| 4110 |  |  | 0F |  |
| 4111 | DLY 1 | MOV R3, #0FH | 7B | Move 0F content now to R3 register. |
| 4112 |  |  | 0F |  |
| 4113 | DLY | DJNZ R3,DLY | DB | If no zero, jump to R3 register for a delay. |
| 4114 |  |  | FE |  |
| 4115 |  | DJNZ R1,DLY1 | D9 | R1 register content is delayed |
| 4116 |  |  | FA |  |
| 4117 |  | DJNZ R2,DLY1 | DA | R2 register content is delayed |
| 4118 |  |  | F8 |  |
| 4119 |  | MOV X@DPTR, A | F0 | Content of A is moved to Acc |
| 411A |  | POP DPL | D0 | L reg content is poped out. |
| 411B |  |  | 82 |  |
| 411C |  | POP DPH | D0 | H reg content is poped out. |
| 411D |  |  | 83 |  |
| 411E |  | INC DPTR | A3 | Increment content of DPTR |
| 411F |  | DJNZ R0, J0 | D8 | Jump the content from J0 to R0. |
| 4120 |  |  | E4 |  |
| 4121 |  | SJUP START | 80 | Jump to start. |
| 4122 |  |  | DD |  |
| 4123 |  | END |  |  |
| 4500 | TABLE | DB | 09 | A clock wise command. |
| 4501 |  |  | 05 |  |
| 4502 |  |  | 06 |  |
| 4503 |  |  | 0A |  |

Result :

Thus the assembly language program for interfacing stepper motor was executed and verified using 8051 microcontroller.

Ex . No :                                                              Interfacing of DC Motor	                                  Page No :

Aim :

To write an assembly language program for interfacing DC motor speed control using 8051 microcontroller.

Apparatus Required :

1.8051 microcontroller kit

2. Keyboard

3.50 core cable

4. DC   motor interface board

5. DC motor

6. Power chord

Algorithm :

- Initialize the data pointer with address FFC0 (DC motor connected address).

- Move the data FF to Accumulator.

- Move the accumulator data to address FFC0.

- Go to step 1.

- Halt the program.

Program :

| ADDRESS | MNEMONICS | OPCODE | COMMENTS |
| --- | --- | --- | --- |
| 4100 | MOV DPTR,#FFCO | 90 | Move the content of FF to the DPTR. |
| 4101 |  | FF |  |
| 4102 |  | C0 | Move the FF content to Acc. |
| 4103 | MOV A,#FF | 74 |  |
| 4104 |  | FF |  |
| 4105 | MOV X@DPTR, A | F0 | Move the X content to Acc. |
| 4106 | SJMP 4100 | 80 | Then jump to the 4100 H address. |
| 4107 |  | F8 |  |

Result :

Thus the assembly language program for interfacing of DC motor was executed and verified using 8051 microcontroller.

Ex . No :                                                                 Interfacing of ADC  		                                  Page No :

Aim :

To write an ALP program for interfacing ADC using 8051 microcontroller.

Apparatus Required :

1.8051 microcontroller kit

2. Keyboard

3.50 core cable

4. ADC Interface board

5.Power chord

Algorithm :

- Initialize the data pointer with address FFC8.

- Select channel 0 in ADC.

- Out the channel address to address FFC8.

- Make the ALE low and High.

- Give SOC signal to ADC.

- Check the EOC pin in ADC (high or not).

- If it is high means read the Digital value from ADC.

- Store the digital value to memory location 4150.

- Halt the program.

Program :

| ADDRESS | LABEL | MNEMONICS | OPCODE | COMMENTS |
| --- | --- | --- | --- | --- |
| 4100 | START | MOV DPTR, #FFC8H | 90 |  |
| 4101 |  |  | FF |  |
| 4102 |  |  | C8 |  |
| 4103 |  | MOV A, #10 | 74 | Select channel 0. |
| 4104 |  |  | 10 |  |
| 4105 |  | MOV X @DPTR,A | F0 | Make ALE low. |
| 4106 |  | MOV A,#18 | 74 | Make ALE high. |
| 4107 |  |  | 18 |  |
| 4108 |  | MOV X @DPTR,A | F0 |  |
| 4109 |  | MOV DPTR, #FFD6 | 90 |  |
| 410A |  |  | FF |  |
| 410B |  |  | D0 |  |
| 410C |  | MOV A,#01 | 74 | SOC signal high. |
| 410D |  |  | 01 |  |
| 410E |  | MOV X @DPTR,A | F0 |  |
| 410F |  | MOV A,#00 | 74 | SOC signal low. |
| 4110 |  |  | 00 |  |
| 4111 |  | MOV X @DPTR,A | F0 |  |
| 4112 |  | MOV DPTR, #FFD8 | 90 |  |
| 4113 |  |  | FF |  |
| 4114 |  |  | D8 |  |
| 4115 | WAIT | MOV X A,@DPTR | E0 |  |
| 4116 |  | JNB E0,WAIT | 30 | Check for EOC. |
| 4117 |  |  | E0 |  |
| 4118 |  |  | FC |  |
| 4119 |  | MOV DPTR, #FFC0 | 90 | Read ADC data. |
| 411A |  |  | FF |  |
| 411B |  |  | C0 |  |
| 411C |  | MOV A,@DPTR | E0 |  |
| 411D |  | MOV DPTR, #4150 | 90 | Store the data in memory. |
| 411E |  |  | 41 |  |
| 411F |  |  | 50 |  |
| 4120 |  | MOV X @DPTR,A | F0 |  |
| 4121 | HERE | SJMP HERE | 80 |  |
| 4122 |  |  | FE |  |

Result :

Thus the assembly language program for interfacing ADC using 8051 was executed and verified successfully.

Ex . No :                                                                 Interfacing of DAC    	                                  Page No :

Aim :

To write an ALP program for interfacing of 8051 microcontroller kit with DAC also to generate the square waveform and triangular waveform.

Apparatus Required :

1.8051 microcontroller kit

2. Keyboard

3.50 core cable

4. DAC interface board

5. Power chord

Algorithm : For Square wave Generation

1. Initialize the data pointer with address FFC8.

2. Move the data 00 accumulator.

3. Out the data to address FFC8.

4. Call delay program

5. Move the data FF to accumulator.

6. Out the data to address FFC8.

7. Call delay program.

8.Go to step 1

9. Halt the program.

Algorithm: For Triangular wave Generation

1. Initialize the data pointer with address FFC8.

2. Move the data 00 accumulator.

3. Out the data to address FFC8.

4. Call delay subroutine Program.

5. Increment the Accumulator data

6. Out the accumulator data to address FFC8 upto Accumulator value

Reaches Zero.

7. Call delay subroutine Program.

8. Go to Step 1.

9. Halt the Program.

Program : Generation of Square Wave

| ADDRESS | LABEL | MNEMONICS | OPCODE | COMMENTS |
| --- | --- | --- | --- | --- |
| 4100 |  | MOV DPTR, #FFC8H | 90 | Move the data to data pointer. |
| 4101 |  |  | FF |  |
| 4102 |  |  | C8 |  |
| 4103 | START | MOV A, #00 | 74 | Move the data to Acc. |
| 4104 |  |  | 00 |  |
| 4105 |  | MOV X @DPTR,A | F0 | Move the data from Acc to DPTR. |
| 4106 |  | LCALL DELAY | 12 | Call DELAY. |
| 4107 |  |  | 41 |  |
| 4108 |  |  | 12 |  |
| 4109 |  | MOV A,#FF | 74 | Move the data to Acc. |
| 410A |  |  | FF |  |
| 410B |  | MOV X @DPTR,A | F0 | Move the data from Acc to DPTR. |
| 410C |  | LCALL DELAY | 12 | Call DELAY. |
| 410D |  |  | 41 |  |
| 410E |  |  | 12 |  |
| 410F |  | LJMP START | 02 | Jump to START. |
| 4110 |  |  | 41 |  |
| 4111 |  |  | 03 |  |
| 4112 | DELAY | MOV R1,#05 | 79 | Move the data to R1 register. |
| 4113 |  |  | 05 |  |
| 4114 | LOOP | MOV R2,#FF | 7A | Move the data to R2 register. |
| 4115 |  |  | FF |  |
| 4116 | HERE | DJNZ R2,HERE | DA | If R2 is not zero, then decrement R2 value and jump to HERE. |
| 4117 |  |  | FE |  |
| 4118 |  | DJNZ R1,LOOP | D9 | If R1 is not zero, then decrement R1 value and jump to LOOP. |
| 4119 |  |  | FA |  |
| 411A |  | RET | 22 | Return |
| 411B |  | SJMP START | 80 | Jump to START. |
| 411C |  |  | E6 |  |

Program : Generation of Triangular Wave

| ADDRESS | LABEL | MNEMONICS | OPCODE | COMMENTS |
| --- | --- | --- | --- | --- |
| 4100 |  | MOV DPTR, #FFC8H | 90 | Move the data to data pointer. |
| 4101 |  |  | FF |  |
| 4102 |  |  | C8 |  |
| 4103 | START | MOV A, #00 | 74 | Move the data to Acc. |
| 4104 |  |  | 00 |  |
| 4105 | LOOP1 | MOV @DPTR,A | F0 | Move the data from Acc to DPTR. |
| 4106 |  | INC A | 04 | Increment the Acc value. |
| 4107 |  | JNZ LOOP1 | 70 | If not zero, then jump to LOOP1. |
| 4108 |  |  | FC |  |
| 4109 |  | MOV A,#FF | 74 | Move the data to Acc. |
| 410A |  |  | FF |  |
| 410B | LOOP2 | MOV X @DPTR,A | F0 | Move the data from Acc to DPTR. |
| 410C |  | DEC A | 14 | Decrement the Acc value. |
| 410D |  | JNZ LOOP2 | 70 | If not zero, then jump to LOOP2. |
| 410E |  |  | FC |  |
| 410F |  | LJMP START | 02 | Jump to START. |
| 4110 |  |  | 41 |  |
| 4111 |  |  | 03 |  |

Result :

Thus the assembly language program for interfacing DAC with 8051 microcontroller was executed and verified.

# Text boxes

Page No:

Page No:

Page No:

Page No:

Page No:

Page No:

Page No:

Page No:

Page No:

Page No:

Page No:

Page No:

Page No:

Page No:

Page No:

Page No:

Page No: